## Slide 1: A Vertical Bubble Flow Network using Inductive-Coupling for 3D CMPs
Hiroki Matsutani1, Yasuhiro Take2, Daisuke Sasaki2,
Masayuki Kimura2, Yuki Ono2, Yukinori Nishiyama2,
Michihiro Koibuchi3, Tadahiro Kuroda2, Hideharu Amano2
1) The University of Tokyo, 2) Keio University,
3) National Institute of Informatics

## Slide 2: Outline: Wireless 3D NoC for CMPs
3D IC technologies
  Wired approach vs. wireless approach
  Inductive-coupling technology
Our target: Wireless 3D CMPs
  Type and number of chips stacked in a package can be customized for given applications
Simple wireless 3D NoC
  Ring-based 3D network
  Bubble flow control
Experimental results
  Real chip implementation
  Full-system simulation results

## Slide 3: Design cost of LSI is increasing
System-on-Chip (SoC)
  Required components are integrated on a single chip
  Different LSI must be developed for each application
System-in-Package (SiP) or 3D IC
  Required components are stacked for each application
By changing the chips in a package, we can provide a wider range of chip family with modest design cost

## Slide 4: 3D IC technology for going vertical
Two chips (face-to-face)
Microbump
Through silicon via
Capacitive coupling
Inductive coupling
Wired
Wireless
More than three chips
Flexibility
Scalability

## Slide 5: Inductive coupling link for 3D ICs
Stacking after chip fabrication
Only know-good-dies selected
Inductor for transceiver
Implemented as a square coil with metal in common CMOS
Not a serious problem. Only
metal layers are occupied
Footprint of inductor
Bonding wires for power supply
More than 3 chips

## Slide 6: An example: MuCCRA-Cube (2008)
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Data Memory
Technology: 90nm, Chip thickness: 85um, Glue: 10um
5.0mm
2.5mm
Inductive-Coupling Up Link
Inductive-Coupling Down Link
4 MuCCRA chips are stacked on a PCB board
[Saito,FPL’09]

## Slide 7: Chip stacking method: Slide & stack
TX
TX
TX
TX
TX
TX
TX
TX
Bonding wire
Bonding wire
Bonding wire
Bonding wire
Inductor has TX/RX/Idle modes (1-cycle switch)
Slide & stack
Inductor (TX)
Inductor (RX)
TX

## Slide 8: Chip stacking method: Slide & stack
TX
TX
TX
TX
TX
TX
TX
TX
Bonding wire
Bonding wire
Bonding wire
Bonding wire
Inductive-coupling link
  Local clock line @ 4GHz
  Serial data line
Inductor (TX)
Inductor (RX)
TX
System clock for NoC is 200MHz
 32-bit transfer for each clock
Local clock is shared by neighboring chips; No global sync.
TxData
TxClk
TxData
TxClk
TxData
TxClk
TxData
TxClk
TxData
TxClk
TxData
TxClk
Today’s talk is the wireless 3D CMP that connects processors & caches using this wireless technology

## Slide 9: Outline: Wireless 3D NoC for CMPs
3D IC technologies
  Wired approach vs. wireless approach
  Inductive-coupling technology
Our target: Wireless 3D CMPs
  Type and number of chips stacked in a package can be customized for given applications
Simple wireless 3D NoC
  Ring-based 3D network
  Bubble flow control
Experimental results
  Real chip implementation
  Full-system simulation results

## Slide 10: Our target: Original 2D CMPs
Chip multi processor (CMP)
  Multiple processors (each has private L1 cache)
  Shared L2 cache divided into multiple banks (SNUCA)
UltraSPARC
L1 cache (I & D)
L2 cache bank
Processor tile
Cache tile

## Slide 11: Our target: Original 2D CMPs
Chip multi processor (CMP)
  Multiple processors (each has private L1 cache)
  Shared L2 cache divided into multiple banks (SNUCA)
  Processors and L2 banks are connected via NoC
On-chip router
UltraSPARC
L1 cache (I & D)
L2 cache bank

## Slide 12: Wireless 3D CMP: Homogeneous
E.g., 2D is divided into 8 planes
  Stacking the same chips
Chip 0
Chip 1
Chip 2
Chip 7

## Slide 13: Wireless 3D CMP: Heterogeneous
Types and number of chips are customized for applications
For memory-bound applications,
  More cache chips are added
For computation-bound applications,
  More processor chips are added
Chip 0
Chip 1
Chip 2
Chip 7
Chips should be added, removed, swapped for given application

## Slide 14: Outline: Wireless 3D NoC for CMPs
3D IC technologies
  Wired approach vs. wireless approach
  Inductive-coupling technology
Our target: Wireless 3D CMPs
  Type and number of chips stacked in a package can be customized for given applications
Simple wireless 3D NoC
  Ring-based 3D network
  Bubble flow control
Experimental results
  Real chip implementation
  Full-system simulation results

## Slide 15: Big picture: Wireless 3D NoC for CMPs
Arbitrary chips are stacked to form a single system
  Each chip has vertical links at pre-specified locations, but we do not know the number and types of chips.
CPU chip from
CPU maker
Memory chip from
memory maker
GPU chip
from
GPU maker
Required chips are stacked for given applications
An example (4 chips)
Ring is the simplest approach to add, remove, swap the nodes
Ring network

## Slide 16: Ring network: Deadlock problems
Ring is the simplest approach to add, remove, and swap the chips in a package without any modifications. But…
Structure deadlock
  Ring network inherently includes a cycle
  Cyclic dependency causes packet deadlocks
Protocol deadlock
  Coherence protocol has multiple message classes
  Request-reply deadlocks
Deadlock-free packet transfer is mandatory for NoCs
RX
TX

## Slide 17: Ring network: VC-based approach
VC-based approach
  Two VCs for each message class
  Packets transit these two VCs at the dateline
Merit
  Conventional VC router
Demerit
  Number of VCs is increased as number of message classes
  6 VCs for 3 classes
Dateline
2VCs for each message class
Cyclic dependency can be cut before and after the dateline by VC transition
RX
TX

## Slide 18: Ring network: Bubble flow approach
Bubble flow approach
  Single buffer can store more than 2 packets
  Buffer space of a single packet is always reserved in each router
Merit
  No VC; Simple flow control
Demerit
  Miss routing when packets cannot exit the ring
  Scalability problem
Single VC that can buffer more than 2 packets
Deadlock does not occur since all buffers are never occupied by the flow control
[Puente,ICPP’99]
[Abad,ISCA’07]
RX
TX

## Slide 19: Outline: Wireless 3D NoC for CMPs
3D IC technologies
  Wired approach vs. wireless approach
  Inductive-coupling technology
Our target: Wireless 3D CMPs
  Type and number of chips stacked in a package can be customized for given applications
Simple wireless 3D NoC
  Ring-based 3D network
  Bubble flow control
Experimental results
  Real chip implementation
  Full-system simulation results

## Slide 20: Test chip implementation @65nm
2.1mm x 2.1mm
Core 0 & 1
Inductors (bus)
Inductors (ring)
Router 0 & 1
Three communication schemes can be tested
  Ring network with VC flow control
  Ring network with Bubble flow control
  Vertical shared bus
Each chip has
  Two cores (packet counter)
  Two routers
  Inductors for ring
  Inductors for vertical bus
Process: Fujitsu 65nm (CS202SZ)
Voltage: 1.2V
System clock: 200MHz

## Slide 21: Test chip implementation @65nm
Core 0 & 1
Inductors (bus)
Inductors (ring)
Router 0 & 1
2.1mm x 2.1mm
Three communication schemes can be tested
  Ring network with VC flow control
  Ring network with Bubble flow control
  Vertical shared bus
TX
Stacking for
Ring network
RX
Slide & stack

## Slide 22: Test chip implementation @65nm
Core 0 & 1
Inductors (bus)
Inductors (ring)
Router 0 & 1
2.1mm x 2.1mm
Three communication schemes can be tested
  Ring network with VC flow control
  Ring network with Bubble flow control
  Vertical shared bus
TX
Stacking for
Ring network
RX
TX/RX
Stacking for
Vertical bus

## Slide 23: Evaluations: Simulation environments
Two network sizes are simulated by GEMS/Simics
4 chips (4-CPU)
3
8 chips (8-CPU)
2
1
0
CPU
L2$ banks
7
1
0
# of chips | 4 / 8
# of CPUs | 4 / 8
# of routers | 8 / 16
# of L2$ banks | 16 / 32
Packet sizes | 1 or 5 flits
Table 1: Architectural parameters
OS | Sun Solaris 9
Compiler | Sun Studio 12
Application | NAS Parallel Bench (OpenMP ver)
Table 2: Software environments
BT, CG, DC, EP, FT, IS, LU, MG, SP, UA (Total 10)
For more detail, refer the paper

## Slide 24: Evaluations: Simulation environments
Two network sizes are simulated by GEMS/Simics
Three communication schemes are compared
Ring + VC flow
Ring + Bubble flow
Vertical bus
4 chips (4-CPU)
3
8 chips (8-CPU)
2
1
0
CPU
L2$ banks
7
1
0
Dateline
2VC

## Slide 25: Results: Network throughput @ 4 chips
RTL simulations of wireless 3D NoC model (8 routers)
Bubble outperforms 2VC(15-flit) & comparable to 2VC(30-flit)
Vertical bus
Ring + VC flow
2VC (15-flit)
Ring + Bubble
Bubble (15-flit)
Bubble(15-flit)
2VC(15-flit)

## Slide 26: Results: Network throughput @ 8 chips
RTL simulations of wireless 3D NoC model (16 routers)
Vertical bus
Ring + VC flow
2VC (15-flit)
Ring + Bubble
Bubble (15-flit)
Bubble(15-flit)
2VC(15-flit)
Bubble outperforms 2VC(15-flit) & comparable to 2VC(30-flit)
Bubble(15-flit)
2VC(15-flit)

## Slide 27: Results: Application performance @4chips
Execution times of NAS parallel bench (4 CPUs)
Ring + VC flow
6VC (30-flit)
Ring + Bubble
Bubble (15-flit)
Ring + VC flow
6VC (18-flit)
Bubble approach outperforms VC-based one by 12.5% @4 chips
Vertical bus
-12.5%

## Slide 28: Results: Application performance @8chips
Execution times of NAS parallel bench (8 CPUs)
Ring + VC flow
6VC (30-flit)
Ring + Bubble
Bubble (15-flit)
Ring + VC flow
6VC (18-flit)
Bubble approach outperforms VC-based one by 7.9% @8 chips
Vertical bus
-7.9%

## Slide 29: Results: Router hardware amount
Placed-and-routed 3-port routers for ring
  6-VC (18-flit) : VC flow control; each VC has 3-flit buf
  6-VC (30-flit) : VC flow control; each VC has 5-flit buf
  Bubble (15-flit) : Bubble flow control; single 15-flit buf
Bubble(15-flit) router is smaller than 6VC(18-flit) by 33.5%
-33.5%

## Slide 30: Summary: Wireless 3D NoC for CMPs
Our target: Wireless 3D CMPs
  Type and number of chips stacked in package can be customized for given applications
Simple wireless 3D NoC for CMPs
  Ring network with VC flow control
  Ring network with Bubble flow control
  Vertical shared bus
Experimental results
  Real chip implementation
  Bubble flow outperforms VC-based one by 7.9%-12.5%
  Bubble router is smaller than VC-based one by 33.5%
Scalability issues remain  New approach with spanning trees